## Slide 1: Payphone Signage Customization
A guide and template
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.

## Slide 2: Orienting yourself to pay phone signage customization
For examples of some traditional payphone visual styles if that is your goal: http://www.phonelosers.org/payphone_inserts/
Typically the Upper Info Card held network or branding information. Occasionally it also included basic usage instructions with an info graphic. Ie 1. Insert coin, 2. Lift receiver. 3. Dial number.
Lower info card held more detailed usage instructions, trouble shooting information and emergency/local numbers.
The number card is what it sounds like the number to call to connect to the company operating the phone.
EACH MODEL VARIES SLIGHTLY BUT THIS IS A VERY TYPICAL LAYOUT ACROSS ATT/WESTERN UNION PHONES. CHECK YOUR PHONE BEFORE FOLLOWING EXACT INSTRUCTIONS.
Upper Info Card
Number Card
Lower Info Card
Some phones have a sticker mounted on the cash box
Phone Company ID sticker

## Slide 3
Printing Instructions: Page should be printed as a pdf at full size. Doc is arranged so all boxes will fit on 8.5x11 or import shapes into design program of your choice.
It is suggested you use heavy weight paper between 100lb – 150lb or that you laminate your paper.
If installing outdoors you may wish to acquire and cut rigid Lexan/polycarbonate sheets to the same size as the cards to protect them.
Guide:
Blue line = cut
Red line = visual boundary
Black line = text box space
Top Information Card: 2.125’’ x 6.4’’
Bottom Information Card: 2.7’’ x 6.4’’
Insert Text Here
Insert Text Here
#-###-###-####
Number Card: .4’’ x 2’’
Template - Customize and Print!

## Slide 4: Installing your Signage
The procedure varies by exact phone. On some models you may be able to just slide the cards into the overhanging lips. On other models there is a card locking screw in the faceplate directly above or below both the lower and upper info cards.
1. Loosen these screws.
2. Insert cards.
3. If using a plastic cover insert.
4. Re-tighten screws.